## 2003 VW B5.5 Passat Wagon GLX 2.8L 2771CC V6    ATQ  GAS MOTOR DOHC Naturally Aspirated.

| Miles (x1000) | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Kilometers (x1000) | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80 | 88 | 96 | 104 | 112 | 120 | 128 | 136 | 144 | 152 | 160 | 168 |
| 2.8L V6 Engine Only |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Engine Oil - Change | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x |
| Engine Filter - Change | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x | x |
| Timing Belt - Check Condition |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  | x |  |  |  |  |  |
| Timing Belt - Replace |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |
| Timing Belt Tensioner - Replace |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |
| V-Belt / Ribbed Belt - check |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  | x |  |  |  |  |  |
| Spark Plugs - Replace |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  | x |  |  |  |  |  |
| All Engines |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Air Cleaner - Replace Filter |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  | x |  |  |  |  |  |
| Windshield Washer Fluid - Check Levels |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Auto-Shift Lock - Check |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Brake System -Check Damage/ Leaks, Pad Thickness, and Fluid Level |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Wheels - Rotate Front to Rear |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Air Bag System - Check Function / Damage * |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Battery - Check Electrolyte Level |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  | x |  |
| Engine - Check for Leaks |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Dust Pollen Filter - Replace |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Cooling System - Check Level |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Manual Transmission - Check for Leaks, add if necessary |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Automatic Transmission - Check for Leaks |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Tires / Spare - Check Condition |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Drive Shafts - Check Boots |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| OBD - Check DTC Memory |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  | x |  |
| Door Hinge - Lubricate |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |